Introduction to Software Defined Network (SDN)
- Srinivas Kodali

---
Outline
Agenda
- Introduction.
- What is Software-Defined Network and Why?
- OpenFlow – quick bite.

---
Traditional Network Router
Present Routers
Router can be partitioned into control and data plane
  - Management plane/ configuration
  - Control plane / Decision: OSPF (Open Shortest Path First)
  - Data plane / Forwarding
Configuration / CLI / GUI
Routing
Control plane
Static routes
OSPF
Neighbor table
Link state database
IP routing table
Switching
Data plane
Forwarding table

---
Imagine IF The Network is……..!!!
SDN - Why……..!!!
SDN: Separate Control plane and Data plane.
Directly Programmable
Centrally Manageable
Agile
Open Standard Based
Control Plane
Logically-centralized control
Smart
API to the data plane
Separated
Dumb,
fast
Switches
Data Plane

---
SDN Basic Concept
SDN Basic Concept
Separate Control plane and Data plane entities.
  - Network intelligence and state are logically centralized.
  - The underlying network infrastructure is abstracted from the applications.
Execute or run Control plane software on general purpose hardware.
  - Decouple from specific networking hardware.
  - Use commodity servers and switches.
- Have programmable data planes.
  - Maintain, control and program data plane state from a central entity.
- An architecture to control not just a networking device but an entire network.

---
SDN Architecture

---
SDN Architectural Components
- SDN Application
  - SDN App logic, NBI Driver
- SDN Controller
  - Translating requirements from SDN App down to the SDN Path.
  - NBI Agent, SDN Controller logic, CDPI Driver
- SDN DataPath
  - CDPI Agent
  - Forwarding Engine(least 1)
  - Processing functions(least 0)
- SDN Control-to-Data Plane Interface(CDPI)
  - Programmatic control of all forwarding operation
  - Capabilities Advertisement
  - Statistics Reporting
  - Event Notification
- SDN North Bound Interface(NBI)
  - Abstraction

---
SDN Control Plane
- Centralized distributed
  - I'm the boss for every one.
- Hierarchical distributed
  - I will take control of few and they will take of sub ordinates
- Fully distributed.
  - We all are equal. We distribute ourselves to score a huge hit.

---
SDN Flow Forwarding
- Reactive mode
  - Flow rule will be added after the request from Switch
- Proactive mode
  - All possible flows will be added before traffic flow
- Hybrid mode
  - Salad of above:)

---
SDN Advantages
- Abstraction :
  - The central controller abstracts the network for you. You don't have to bother about the underlying data plane.
- Virtualization :
  - Abstraction derives the virtualization.
- Orchestration:
  - Single command or API call to the controller from the application layer is needed.
- Automation :
  - One of the factor which incurs huge costs in networks, is operational cost . Automation is anyday preferred. Using SDN, Automation of many tasks like Policy enforcement, Feature Addition, New Protocol Support etc can be automated.

---
SDN Advantages
- Performance :
  - Lot of applications like Load Balancing, Traffic Engineering methods , Capacity optimization can be deployed on the SDN .
- New Protocol Support:
  - With the advent of P4 and OpenFlow 2.0 designing and deploying new protocols on to the switches is really cool and easy.

---
SDN Challenges
One of the major challenge encountered in implementing SDN is the support from the router/switch companies. Nobody likes their devices to be dumb. But consumers want support and dumb devices as well. It's a deadlock

---
SDN in Real World – Google’s Story
SDN in Real World – Google’s Story
- The industries were skeptical whether SDN was possible.
- Google had big problems:
  - High financial cost managing their datacenters: Hardware and software upgrade, over provisioning (fault tolerant), manage large backup traffic, time to manage individual switch, and a lot of men power to manage the infrastructure.
  - Delay caused by rebuilding connections after link failure.
    - Slow to rebuild the routing tables after link failure.
    - Difficult to predict what the new network may perform.
- Google went a head and implemented SDN.
  - Built their hardware and wrote their own software for their internal datacenters.
  - Surprised the industries when Google announced SDN was possible in production.

---
The Origin of SDN
The Origin of SDN
- Martin Casado
- 2006: Martin Casado, a PhD student at Stanford and team propose a clean-slate security architecture (SANE) which defines a centralized control of security (in stead of at the edge as normally done).
- 2008: The idea of Software Defined Network is originated from OpenFlow project.
- 2009: Stanford publishes OpenFlow V1.0.0 specs.
- 2009: Martin Casado co-founds Nicira.
- 2011: Open Networking Foundation is formed.
- 2011: First Open Networking Summit. Many Industries (Juniper, Cisco announced to incorporate.
- 2012: VMware buys Nicira.

---
What is OpenFlow?
What is OpenFlow?
Application B
Application A
 Control Plane (Network OS)
OpenFlow Protocols
Control Path
OpenFlow
Data Path (Hardware)
Data Plane

---
What is OpenFlow?
What is OpenFlow?
- Allow separation of control and data planes.
- Centralization of control.
- Flow based control.
- Takes advantage routing tables in Ethernet switches and routers.
SDN is not OpenFlow.
  - SDN is a concept of the physical separation of the network control plane from the forwarding plane, and where a control plane controls several devices.
  - OpenFlow is communication interface between the control and data plane of an SDN architecture.
    - Allows direct access to and manipulation of the forwarding plane of network devices such as switches and routers, both physical and virtual.
[Speaker Notes: OpenFlow is a communications protocol that gives access to the forwarding plane of a network switch or router over the network]

---
Switches That Support OpenFlow
Available OpenFlow Switches.
Juniper MX-series
NEC IP8800
WiMax (NEC)
HP Procurve 5400
Netgear 7324
PC Engines
Pronto 3240/3290
Ciena Coredirector
[Speaker Notes: Not only switches but other network components]

---
OpenFlow Switch Software
OpenFlow Switch Software
- Indigo: Open source implementation that runs on Mac OS X.
- LINC: Open source implementation that runs on Linux, Solaris, Windows, MacOS, and FreeBSD.
- Pantou: Turns a commercial wireless router/access point to an OpenFlow enabled switch. OpenFlow runs on OpenWRT. Supports generic Broadcom and some models of LinkSys and TP-Link access points with Broadcom and Atheros chipsets.
- Of13softswitch: User-space software switch based on Ericsson TrafficLab 1.1 softswitch.
- Open vSwitch: Open Source and popular as 2014.

---
Controller Plane Software
Controller Plane Software
- POX: (Python) Out of Date.
- IRIS: (Java) Scalability and High Availability
- MUL: (C) MūL, is an openflow (SDN) controller. It has a C based multi-threaded infrastructure at its core.
- NOX: (C++/Python) NOX was the first OpenFlow controller.
- Jaxon: (Java) Jaxon is a NOX-dependent Java-based OpenFlow Controller.
- Trema: (C/Ruby) Trema is a full-stack framework for developing OpenFlow controllers in Ruby and C.
- Beacon: (Java) Beacon supports both event-based and threaded operation.
- Floodlight: (Java) It was forked from the Beacon controller, originally developed by David Erickson at Stanford.
- And many more.

---
Conclusion
Conclusion
Key ideas of SDN:
  - Dynamic programmability in forwarding packets.
  - Decoupling control and data plane.
  - Global view network by logical centralization in control plane.
  - Applications can be implemented on top of the control plane.
  - SDN is a concept to manage network that leverages OpenFlow protocols.

---
Question????
Questions????
Thank you