A. OSPF data formats

    This appendix describes the format of OSPF protocol packets and OSPF
    LSAs. The OSPF protocol runs directly over the IP network layer.
    Before any data formats are described, the details of the OSPF
    encapsulation are explained.

    Next the OSPF Options field is described. This field describes
    various capabilities that may or may not be supported by pieces of
    the OSPF routing domain. The OSPF Options field is contained in OSPF
    Hello packets, Database Description packets and in OSPF LSAs.

    OSPF packet formats are detailed in Section A.3. A description of
    OSPF LSAs appears in Section A.4.

A.1 Encapsulation of OSPF packets

    OSPF runs directly over the Internet Protocol's network layer. OSPF
    packets are therefore encapsulated solely by IP and local data-link
    headers.

    OSPF does not define a way to fragment its protocol packets, and
    depends on IP fragmentation when transmitting packets larger than
    the network MTU. If necessary, the length of OSPF packets can be up
    to 65,535 bytes (including the IP header). The OSPF packet types
    that are likely to be large (Database Description Packets, Link
    State Request, Link State Update, and Link State Acknowledgment
    packets) can usually be split into several separate protocol
    packets, without loss of functionality. This is recommended; IP
    fragmentation should be avoided whenever possible. Using this
    reasoning, an attempt should be made to limit the sizes of OSPF
    packets sent over virtual links to 576 bytes unless Path MTU
    Discovery is being performed (see [Ref22]).

    The other important features of OSPF's IP encapsulation are:

    o Use of IP multicast. Some OSPF messages are multicast, when
        sent over broadcast networks. Two distinct IP multicast
        addresses are used. Packets sent to these multicast addresses
        should never be forwarded; they are meant to travel a single hop
        only. To ensure that these packets will not travel multiple
        hops, their IP TTL must be set to 1.

        AllSPFRouters
        This multicast address has been assigned the value
        224.0.0.5. All routers running OSPF should be prepared to
        receive packets sent to this address. Hello packets are
        always sent to this destination. Also, certain OSPF
        protocol packets are sent to this address during the
        flooding procedure.

        AllDRouters
        This multicast address has been assigned the value
        224.0.0.6. Both the Designated Router and Backup Designated
        Router must be prepared to receive packets destined to this
        address. Certain OSPF protocol packets are sent to this
        address during the flooding procedure.

    o OSPF is IP protocol number 89. This number has been registered
        with the Network Information Center. IP protocol number
        assignments are documented in [Ref11].

    o All OSPF routing protocol packets are sent using the normal
        service TOS value of binary 0000 defined in [Ref12].

    o Routing protocol packets are sent with IP precedence set to
        Internetwork Control. OSPF protocol packets should be given
        precedence over regular IP data traffic, in both sending and
        receiving. Setting the IP precedence field in the IP header to
        Internetwork Control [Ref5] may help implement this objective.

A.2 The Options field

    The OSPF Options field is present in OSPF Hello packets, Database
    Description packets and all LSAs. The Options field enables OSPF
    routers to support (or not support) optional capabilities, and to
    communicate their capability level to other OSPF routers. Through
    this mechanism routers of differing capabilities can be mixed within
    an OSPF routing domain.

    When used in Hello packets, the Options field allows a router to
    reject a neighbor because of a capability mismatch. Alternatively,
    when capabilities are exchanged in Database Description packets a
    router can choose not to forward certain LSAs to a neighbor because
    of its reduced functionality. Lastly, listing capabilities in LSAs
    allows routers to forward traffic around reduced functionality
    routers, by excluding them from parts of the routing table
    calculation.

    Five bits of the OSPF Options field have been assigned, although
    only one (the E-bit) is described completely by this memo. Each bit
    is described briefly below. Routers should reset (i.e. clear)
    unrecognized bits in the Options field when sending Hello packets or
    Database Description packets and when originating LSAs. Conversely,
    routers encountering unrecognized Option bits in received Hello
    Packets, Database Description packets or LSAs should ignore the
    capability and process the packet/LSA normally.

        +------------------------------------+
        | * | * | DC | EA | N/P | MC | E | * |
        +------------------------------------+

        The Options field

    E-bit
        This bit describes the way AS-external-LSAs are flooded, as
        described in Sections 3.6, 9.5, 10.8 and 12.1.2 of this memo.

    MC-bit
        This bit describes whether IP multicast datagrams are forwarded
        according to the specifications in [Ref18].

    N/P-bit
        This bit describes the handling of Type-7 LSAs, as specified in
        [Ref19].

    EA-bit
        This bit describes the router's willingness to receive and
        forward External-Attributes-LSAs, as specified in [Ref20].

    DC-bit
        This bit describes the router's handling of demand circuits, as
        specified in [Ref21].

A.3 OSPF Packet Formats

    There are five distinct OSPF packet types. All OSPF packet types
    begin with a standard 24 byte header. This header is described
    first. Each packet type is then described in a succeeding section.
    In these sections each packet's division into fields is displayed,
    and then the field definitions are enumerated.

    All OSPF packet types (other than the OSPF Hello packets) deal with
    lists of LSAs. For example, Link State Update packets implement the
    flooding of LSAs throughout the OSPF routing domain. Because of
    this, OSPF protocol packets cannot be parsed unless the format of
    LSAs is also understood. The format of LSAs is described in Section
    A.4.

    The receive processing of OSPF packets is detailed in Section 8.2.
    The sending of OSPF packets is explained in Section 8.1.

A.3.1 The OSPF packet header

    Every OSPF packet starts with a standard 24 byte header. This
    header contains all the information necessary to determine whether
    the packet should be accepted for further processing. This
    determination is described in Section 8.2 of the specification.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Version # | Type | Packet length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Router ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Area ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Checksum | AuType |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

    Version #
        The OSPF version number. This specification documents version 2
        of the protocol.

    Type
        The OSPF packet types are as follows. See Sections A.3.2 through
        A.3.6 for details.

        Type Description
        ________________________________
        1 Hello
        2 Database Description
        3 Link State Request
        4 Link State Update
        5 Link State Acknowledgment

    Packet length
        The length of the OSPF protocol packet in bytes. This length
        includes the standard OSPF header.

    Router ID
        The Router ID of the packet's source.

    Area ID
        A 32 bit number identifying the area that this packet belongs
        to. All OSPF packets are associated with a single area. Most
        travel a single hop only. Packets travelling over a virtual
        link are labelled with the backbone Area ID of 0.0.0.0.

    Checksum
        The standard IP checksum of the entire contents of the packet,
        starting with the OSPF packet header but excluding the 64-bit
        authentication field. This checksum is calculated as the 16-bit
        one's complement of the one's complement sum of all the 16-bit
        words in the packet, excepting the authentication field. If the
        packet's length is not an integral number of 16-bit words, the
        packet is padded with a byte of zero before checksumming. The
        checksum is considered to be part of the packet authentication
        procedure; for some authentication types the checksum
        calculation is omitted.

    AuType
        Identifies the authentication procedure to be used for the
        packet. Authentication is discussed in Appendix D of the
        specification. Consult Appendix D for a list of the currently
        defined authentication types.

    Authentication
        A 64-bit field for use by the authentication scheme. See
        Appendix D for details.

A.3.2 The Hello packet

    Hello packets are OSPF packet type 1. These packets are sent
    periodically on all interfaces (including virtual links) in order to
    establish and maintain neighbor relationships. In addition, Hello
    Packets are multicast on those physical networks having a multicast
    or broadcast capability, enabling dynamic discovery of neighboring
    routers.

    All routers connected to a common network must agree on certain
    parameters (Network mask, HelloInterval and RouterDeadInterval).
    These parameters are included in Hello packets, so that differences
    can inhibit the forming of neighbor relationships. A detailed
    explanation of the receive processing for Hello packets is presented
    in Section 10.5. The sending of Hello packets is covered in Section
    9.5.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Version # | 1 | Packet length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Router ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Area ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Checksum | AuType |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Network Mask |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | HelloInterval | Options | Rtr Pri |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | RouterDeadInterval |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Designated Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Backup Designated Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Neighbor |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    Network mask
        The network mask associated with this interface. For example,
        if the interface is to a class B network whose third byte is
        used for subnetting, the network mask is 0xffffff00.

    Options
        The optional capabilities supported by the router, as documented
        in Section A.2.

    HelloInterval
        The number of seconds between this router's Hello packets.

    Rtr Pri
        This router's Router Priority. Used in (Backup) Designated
        Router election. If set to 0, the router will be ineligible to
        become (Backup) Designated Router.

    RouterDeadInterval
        The number of seconds before declaring a silent router down.

    Designated Router
        The identity of the Designated Router for this network, in the
        view of the sending router. The Designated Router is identified
        here by its IP interface address on the network. Set to 0.0.0.0
        if there is no Designated Router.

    Backup Designated Router
        The identity of the Backup Designated Router for this network,
        in the view of the sending router. The Backup Designated Router
        is identified here by its IP interface address on the network.
        Set to 0.0.0.0 if there is no Backup Designated Router.

    Neighbor
        The Router IDs of each router from whom valid Hello packets have
        been seen recently on the network. Recently means in the last
        RouterDeadInterval seconds.

A.3.3 The Database Description packet

    Database Description packets are OSPF packet type 2. These packets
    are exchanged when an adjacency is being initialized. They describe
    the contents of the link-state database. Multiple packets may be
    used to describe the database. For this purpose a poll-response
    procedure is used. One of the routers is designated to be the
    master, the other the slave. The master sends Database Description
    packets (polls) which are acknowledged by Database Description
    packets sent by the slave (responses). The responses are linked to
    the polls via the packets' DD sequence numbers.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Version # | 2 | Packet length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Router ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Area ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Checksum | AuType |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Interface MTU | Options |0|0|0|0|0|I|M|MS
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | DD sequence number |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | |
       +- -+
       | |
       +- An LSA Header -+
       | |
       +- -+
       | |
       +- -+
       | |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

Moy Standards Track [Page 195]

RFC 2328 OSPF Version 2 April 1998

    The format of the Database Description packet is very similar to
    both the Link State Request and Link State Acknowledgment packets.
    The main part of all three is a list of items, each item describing
    a piece of the link-state database. The sending of Database
    Description Packets is documented in Section 10.8. The reception of
    Database Description packets is documented in Section 10.6.

    Interface MTU
        The size in bytes of the largest IP datagram that can be sent
        out the associated interface, without fragmentation. The MTUs
        of common Internet link types can be found in Table 7-1 of
        [Ref22]. Interface MTU should be set to 0 in Database
        Description packets sent over virtual links.

    Options
        The optional capabilities supported by the router, as documented
        in Section A.2.

    I-bit
        The Init bit. When set to 1, this packet is the first in the
        sequence of Database Description Packets.

    M-bit
        The More bit. When set to 1, it indicates that more Database
        Description Packets are to follow.

    MS-bit
        The Master/Slave bit. When set to 1, it indicates that the
        router is the master during the Database Exchange process.
        Otherwise, the router is the slave.

    DD sequence number
        Used to sequence the collection of Database Description Packets.
        The initial value (indicated by the Init bit being set) should
        be unique. The DD sequence number then increments until the
        complete database description has been sent.

    The rest of the packet consists of a (possibly partial) list of the
    link-state database's pieces. Each LSA in the database is described
    by its LSA header. The LSA header is documented in Section A.4.1.
    It contains all the information required to uniquely identify both
    the LSA and the LSA's current instance.

A.3.4 The Link State Request packet

    Link State Request packets are OSPF packet type 3. After exchanging
    Database Description packets with a neighboring router, a router may
    find that parts of its link-state database are out-of-date. The
    Link State Request packet is used to request the pieces of the
    neighbor's database that are more up-to-date. Multiple Link State
    Request packets may need to be used.

    A router that sends a Link State Request packet has in mind the
    precise instance of the database pieces it is requesting. Each
    instance is defined by its LS sequence number, LS checksum, and LS
    age, although these fields are not specified in the Link State
    Request Packet itself. The router may receive even more recent
    instances in response.

    The sending of Link State Request packets is documented in Section
    10.9. The reception of Link State Request packets is documented in
    Section 10.7.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Version # | 3 | Packet length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Router ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Area ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Checksum | AuType |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS type |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link State ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Advertising Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    Each LSA requested is specified by its LS type, Link State ID, and
    Advertising Router. This uniquely identifies the LSA, but not its
    instance. Link State Request packets are understood to be requests
    for the most recent instance (whatever that might be).

A.3.5 The Link State Update packet

    Link State Update packets are OSPF packet type 4. These packets
    implement the flooding of LSAs. Each Link State Update packet
    carries a collection of LSAs one hop further from their origin.
    Several LSAs may be included in a single packet.

    Link State Update packets are multicast on those physical networks
    that support multicast/broadcast. In order to make the flooding
    procedure reliable, flooded LSAs are acknowledged in Link State
    Acknowledgment packets. If retransmission of certain LSAs is
    necessary, the retransmitted LSAs are always sent directly to the
    neighbor. For more information on the reliable flooding of LSAs,
    consult Section 13.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Version # | 4 | Packet length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Router ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Area ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Checksum | AuType |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | # LSAs |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | |
       +- +-+
       | LSAs |
       +- +-+
       | ... |

    # LSAs
        The number of LSAs included in this update.

    The body of the Link State Update packet consists of a list of LSAs.
    Each LSA begins with a common 20 byte header, described in Section
    A.4.1. Detailed formats of the different types of LSAs are described
    in Section A.4.

A.3.6 The Link State Acknowledgment packet

    Link State Acknowledgment Packets are OSPF packet type 5. To make
    the flooding of LSAs reliable, flooded LSAs are explicitly
    acknowledged. This acknowledgment is accomplished through the
    sending and receiving of Link State Acknowledgment packets.
    Multiple LSAs can be acknowledged in a single Link State
    Acknowledgment packet.

    Depending on the state of the sending interface and the sender of
    the corresponding Link State Update packet, a Link State
    Acknowledgment packet is sent either to the multicast address
    AllSPFRouters, to the multicast address AllDRouters, or as a
    unicast. The sending of Link State Acknowledgement packets is
    documented in Section 13.5. The reception of Link State
    Acknowledgement packets is documented in Section 13.7.

    The format of this packet is similar to that of the Data Description
    packet. The body of both packets is simply a list of LSA headers.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Version # | 5 | Packet length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Router ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Area ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Checksum | AuType |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Authentication |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | |
       +- -+
       | |
       +- An LSA Header -+
       | |
       +- -+
       | |
       +- -+
       | |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    Each acknowledged LSA is described by its LSA header. The LSA
    header is documented in Section A.4.1. It contains all the
    information required to uniquely identify both the LSA and the LSA's
    current instance.

A.4 LSA formats

    This memo defines five distinct types of LSAs. Each LSA begins with
    a standard 20 byte LSA header. This header is explained in Section
    A.4.1. Succeeding sections then diagram the separate LSA types.

    Each LSA describes a piece of the OSPF routing domain. Every router
    originates a router-LSA. In addition, whenever the router is
    elected Designated Router, it originates a network-LSA. Other types
    of LSAs may also be originated (see Section 12.4). All LSAs are
    then flooded throughout the OSPF routing domain. The flooding
    algorithm is reliable, ensuring that all routers have the same
    collection of LSAs. (See Section 13 for more information concerning
    the flooding algorithm). This collection of LSAs is called the
    link-state database.

    From the link state database, each router constructs a shortest path
    tree with itself as root. This yields a routing table (see Section
    11). For the details of the routing table build process, see
    Section 16.

A.4.1 The LSA header

    All LSAs begin with a common 20 byte header. This header contains
    enough information to uniquely identify the LSA (LS type, Link State
    ID, and Advertising Router). Multiple instances of the LSA may
    exist in the routing domain at the same time. It is then necessary
    to determine which instance is more recent. This is accomplished by
    examining the LS age, LS sequence number and LS checksum fields that
    are also contained in the LSA header.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS age | Options | LS type |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link State ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Advertising Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS sequence number |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS checksum | length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

    LS age
        The time in seconds since the LSA was originated.

    Options
        The optional capabilities supported by the described portion of
        the routing domain. OSPF's optional capabilities are documented
        in Section A.2.

    LS type
        The type of the LSA. Each LSA type has a separate advertisement
        format. The LSA types defined in this memo are as follows (see
        Section 12.1.3 for further explanation):

        LS Type Description
        ___________________________________
        1 Router-LSAs
        2 Network-LSAs
        3 Summary-LSAs (IP network)
        4 Summary-LSAs (ASBR)
        5 AS-external-LSAs

    Link State ID
        This field identifies the portion of the internet environment
        that is being described by the LSA. The contents of this field
        depend on the LSA's LS type. For example, in network-LSAs the
        Link State ID is set to the IP interface address of the
        network's Designated Router (from which the network's IP address
        can be derived). The Link State ID is further discussed in
        Section 12.1.4.

    Advertising Router
        The Router ID of the router that originated the LSA. For
        example, in network-LSAs this field is equal to the Router ID of
        the network's Designated Router.

    LS sequence number
        Detects old or duplicate LSAs. Successive instances of an LSA
        are given successive LS sequence numbers. See Section 12.1.6
        for more details.

    LS checksum
        The Fletcher checksum of the complete contents of the LSA,
        including the LSA header but excluding the LS age field. See
        Section 12.1.7 for more details.

    length
        The length in bytes of the LSA. This includes the 20 byte LSA
        header.

A.4.2 Router-LSAs

    Router-LSAs are the Type 1 LSAs. Each router in an area originates
    a router-LSA. The LSA describes the state and cost of the router's
    links (i.e., interfaces) to the area. All of the router's links to
    the area must be described in a single router-LSA. For details
    concerning the construction of router-LSAs, see Section 12.4.1.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS age | Options | 1 |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link State ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Advertising Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS sequence number |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS checksum | length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | 0 |V|E|B| 0 | # links |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link Data |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Type | # TOS | metric |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | TOS | 0 | TOS metric |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link Data |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    In router-LSAs, the Link State ID field is set to the router's OSPF
    Router ID. Router-LSAs are flooded throughout a single area only.

    bit V
        When set, the router is an endpoint of one or more fully
        adjacent virtual links having the described area as Transit area
        (V is for virtual link endpoint).

    bit E
        When set, the router is an AS boundary router (E is for
        external).

    bit B
        When set, the router is an area border router (B is for border).

    # links
        The number of router links described in this LSA. This must be
        the total collection of router links (i.e., interfaces) to the
        area.

    The following fields are used to describe each router link (i.e.,
    interface). Each router link is typed (see the below Type field).
    The Type field indicates the kind of link being described. It may
    be a link to a transit network, to another router or to a stub
    network. The values of all the other fields describing a router
    link depend on the link's Type. For example, each link has an
    associated 32-bit Link Data field. For links to stub networks this
    field specifies the network's IP address mask. For other link types
    the Link Data field specifies the router interface's IP address.

    Type
        A quick description of the router link. One of the following.
        Note that host routes are classified as links to stub networks
        with network mask of 0xffffffff.

        Type Description
        __________________________________________________
        1 Point-to-point connection to another router
        2 Connection to a transit network
        3 Connection to a stub network
        4 Virtual link

    Link ID
        Identifies the object that this router link connects to. Value
        depends on the link's Type. When connecting to an object that
        also originates an LSA (i.e., another router or a transit
        network) the Link ID is equal to the neighboring LSA's Link
        State ID. This provides the key for looking up the neighboring
        LSA in the link state database during the routing table
        calculation. See Section 12.2 for more details.

        Type Link ID
        ______________________________________
        1 Neighboring router's Router ID
        2 IP address of Designated Router
        3 IP network/subnet number
        4 Neighboring router's Router ID

    Link Data
        Value again depends on the link's Type field. For connections to
        stub networks, Link Data specifies the network's IP address
        mask. For unnumbered point-to-point connections, it specifies
        the interface's MIB-II [Ref8] ifIndex value. For the other link
        types it specifies the router interface's IP address. This
        latter piece of information is needed during the routing table
        build process, when calculating the IP address of the next hop.
        See Section 16.1.1 for more details.

    # TOS
        The number of different TOS metrics given for this link, not
        counting the required link metric (referred to as the TOS 0
        metric in [Ref9]). For example, if no additional TOS metrics
        are given, this field is set to 0.

    metric
        The cost of using this router link.

    Additional TOS-specific information may also be included, for
    backward compatibility with previous versions of the OSPF
    specification ([Ref9]). Within each link, and for each desired TOS,
    TOS TOS-specific link information may be encoded as follows:

    TOS IP Type of Service that this metric refers to. The encoding of
        TOS in OSPF LSAs is described in Section 12.3.

    TOS metric
        TOS-specific metric information.

A.4.3 Network-LSAs

    Network-LSAs are the Type 2 LSAs. A network-LSA is originated for
    each broadcast and NBMA network in the area which supports two or
    more routers. The network-LSA is originated by the network's
    Designated Router. The LSA describes all routers attached to the
    network, including the Designated Router itself. The LSA's Link
    State ID field lists the IP interface address of the Designated
    Router.

    The distance from the network to all attached routers is zero. This
    is why metric fields need not be specified in the network-LSA. For
    details concerning the construction of network-LSAs, see Section
    12.4.2.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS age | Options | 2 |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link State ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Advertising Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS sequence number |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS checksum | length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Network Mask |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Attached Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    Network Mask
        The IP address mask for the network. For example, a class A
        network would have the mask 0xff000000.

    Attached Router
        The Router IDs of each of the routers attached to the network.
        Actually, only those routers that are fully adjacent to the
        Designated Router are listed. The Designated Router includes
        itself in this list. The number of routers included can be
        deduced from the LSA header's length field.

A.4.4 Summary-LSAs

    Summary-LSAs are the Type 3 and 4 LSAs. These LSAs are originated
    by area border routers. Summary-LSAs describe inter-area
    destinations. For details concerning the construction of summary-
    LSAs, see Section 12.4.3.

    Type 3 summary-LSAs are used when the destination is an IP network.
    In this case the LSA's Link State ID field is an IP network number
    (if necessary, the Link State ID can also have one or more of the
    network's "host" bits set; see Appendix E for details). When the
    destination is an AS boundary router, a Type 4 summary-LSA is used,
    and the Link State ID field is the AS boundary router's OSPF Router
    ID. (To see why it is necessary to advertise the location of each
    ASBR, consult Section 16.4.) Other than the difference in the Link
    State ID field, the format of Type 3 and 4 summary-LSAs is
    identical.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS age | Options | 3 or 4 |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link State ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Advertising Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS sequence number |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS checksum | length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Network Mask |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | 0 | metric |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | TOS | TOS metric |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    For stub areas, Type 3 summary-LSAs can also be used to describe a
    (per-area) default route. Default summary routes are used in stub
    areas instead of flooding a complete set of external routes. When
    describing a default summary route, the summary-LSA's Link State ID
    is always set to DefaultDestination (0.0.0.0) and the Network Mask
    is set to 0.0.0.0.

    Network Mask
        For Type 3 summary-LSAs, this indicates the destination
        network's IP address mask. For example, when advertising the
        location of a class A network the value 0xff000000 would be
        used. This field is not meaningful and must be zero for Type 4
        summary-LSAs.

    metric
        The cost of this route. Expressed in the same units as the
        interface costs in the router-LSAs.

    Additional TOS-specific information may also be included, for
    backward compatibility with previous versions of the OSPF
    specification ([Ref9]). For each desired TOS, TOS-specific
    information is encoded as follows:

    TOS IP Type of Service that this metric refers to. The encoding of
        TOS in OSPF LSAs is described in Section 12.3.

    TOS metric
        TOS-specific metric information.

A.4.5 AS-external-LSAs

    AS-external-LSAs are the Type 5 LSAs. These LSAs are originated by
    AS boundary routers, and describe destinations external to the AS.
    For details concerning the construction of AS-external-LSAs, see
    Section 12.4.3.

    AS-external-LSAs usually describe a particular external destination.
    For these LSAs the Link State ID field specifies an IP network
    number (if necessary, the Link State ID can also have one or more of
    the network's "host" bits set; see Appendix E for details). AS-
    external-LSAs are also used to describe a default route. Default
    routes are used when no specific route exists to the destination.
    When describing a default route, the Link State ID is always set to
    DefaultDestination (0.0.0.0) and the Network Mask is set to 0.0.0.0.

        0 1 2 3
        0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS age | Options | 5 |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Link State ID |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Advertising Router |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS sequence number |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | LS checksum | length |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Network Mask |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       |E| 0 | metric |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Forwarding address |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | External Route Tag |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       |E| TOS | TOS metric |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | Forwarding address |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | External Route Tag |
       +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
       | ... |

    Network Mask
        The IP address mask for the advertised destination. For
        example, when advertising a class A network the mask 0xff000000
        would be used.

    bit E
        The type of external metric. If bit E is set, the metric
        specified is a Type 2 external metric. This means the metric is
        considered larger than any link state path. If bit E is zero,
        the specified metric is a Type 1 external metric. This means
        that it is expressed in the same units as the link state metric
        (i.e., the same units as interface cost).

    metric
        The cost of this route. Interpretation depends on the external
        type indication (bit E above).

    Forwarding address
        Data traffic for the advertised destination will be forwarded to
        this address. If the Forwarding address is set to 0.0.0.0, data
        traffic will be forwarded instead to the LSA's originator (i.e.,
        the responsible AS boundary router).

    External Route Tag
        A 32-bit field attached to each external route. This is not
        used by the OSPF protocol itself. It may be used to communicate
        information between AS boundary routers; the precise nature of
        such information is outside the scope of this specification.

    Additional TOS-specific information may also be included, for
    backward compatibility with previous versions of the OSPF
    specification ([Ref9]). For each desired TOS, TOS-specific
    information is encoded as follows:

    TOS The Type of Service that the following fields concern. The
        encoding of TOS in OSPF LSAs is described in Section 12.3.
    bit E
        For backward-compatibility with [Ref9].

    TOS metric
        TOS-specific metric information.

    Forwarding address
        For backward-compatibility with [Ref9].

    External Route Tag
        For backward-compatibility with [Ref9].